David Bailleux

Laser status, March 2009

For CMS week

- B-field solutions:

- Power meter ordered

- New digital INFRARED viewer received

- 1 digital scope already in hand (waiting B field to test)

- One AC control unit has to be moved inside the room (waiting B field for action)

- Shielding around power supply and pump laser (lamp):  already defined

- Software interlock on lamp with fast dump: not yet defined.

e & f ( main tasks to be ready before magnet field

- Cooling circuit:

New cooling circuit tested but can’t be used:

- leak detection not working (but no leak detection up to know)

- missing “vanne de regulation”: pump is stopping is there is no more flow

- Waiting connection for pump command on electrical cupboard

- DCS not tested

Maybe more news this week on schedule.

- Others tasks:

a. DCS, to connected room temperature probes:

- CanBus installed;

- Read out done via central DCS: waiting.

b. Laser supervisor PC:

Reboot PC remotely not yet done; (Bad configuration last week on this PC, no access anymore ( no laser RUN)

Waiting for an AC smart control Unit to turn ON/OFF devices (PC, GPib, ect.)

c. Need laser interface to DCS / PVSS to got laser status.